INTERNET PROTOCOL ADDRESS (IP ADDRESS)
IP Versions :-
IP v4
IP v6
IP v4 :-
In IPv4 an address consists of 32 bits.
IPv4 addresses are canonically represented in dot decimal notation.
Ranging from 0 to 255. e.g. 172.16.254.1
Each have 8 octets.
Starts from 0.0.0.0 to 255.255.255.255
Class A,B,C,D & E

---
Class A – 1 to 126
Subnet mask 255.0.0.0 e.g :- 10.0.0.0
Host
N/W
127 – Loop Back
Class B – 128 to 191
Subnet mask 255.255.0.0 e.g :- 128.16.0.0
N/W
Host
169 – APIPA
Class C – 192 to 223
Subnet mask 255.255.255.0 e.g :- 192.168.2.0
N/W
Host
Class D – 224 to 239 - Multicast
Class E – 240 to 225 – Research Purpose

---
Private IP v4 Range :-
Class A – 10.0.0.0 to 10.255.255.255 (Total 16,777,216 IP Address)
Class B – 172.16.0.0 to 172.31.255.255 (Total 1,048,576 IP Address)
Class C – 192.168.0.0 to 192.168.255.255 (Total 65,536 IP Address)

---
SUBNETTING :-
Dividing a network into two or more networks is called subnetting.
Logical subdivision of an IP network.
Steps to do subnetting …!!!
m = no. of bits taken for subnetting.
n = remaining bits in the host part.
2^m = no. of networks.
2^n-2 = no. of hosts per subnet.
2^n = block size
Mark portion = 256 minus (-) Block Size
New Subnet Mask = Default Mask + Mask portion in the subnetted octet.
First Network = parent network + Block size in the subnetted octet.
First host of the first network = First network + 1 in the last octet.
First network broadcast = Second network minus (-) 1 in the last octet.
Last host of the First network = Broadcast minus (-) 1 in the last octet.

---
Next Network = First network + block size in the subnetted octet.
Last Network = Mask portion minus (-) Block size in the subnetted octet.
Last Network = Mask portion minus (-) Block size in the subnetted octet.
Broadcast of last network = mask portion minus (-) 1 in the subnetted octet.
e.g.
Class C ==>
192.168.1.0 → Parent n/w
255.255.255.0
Host (00000000)
192.168.1.0/25
24 + 1 = 25
Host 0] 0000000
m = 1 (no. of bits taken for subnetting).
n = 7 (remaining bits in the host portion).
2^n-1= 2^7 - 2 = 128 – 2 = 126 (hosts per network).
2^m = 2^1 = 2 (no. of sub networks).

---
2^m Block size = 128 i.e 256 – 128 = 128
First host IP ==> 192.168.1.0 (Plus 1)
     192.168.1.1(First host IP address)
*
*
*
192.168.1.126 (last host IP address)
192.168.1.127 ( Broadcast IP address)
Last network ==> 192.168.1.128 (next network)
 192.168.1.129 (First host)
*
*
*
 192.168.1.254 (Last host)
  192.168.1.255 (Broadcast IP)
Subnet mask for both network → 255.255.255.128

---
Class B ==> 172.16.0.0 / 17
0] 0000000
2^1 = 2 (no. of subnets)
2^m = 2^7 = 128
no. of host per subnet = 2^n – 2 = 128-2 = 126
Block size = 256 – 126 = 128
Subnet mask ==> 255.255.128.255
172.16.0.0 (First network)
      172.16.0.1 (First IP)
*
*
*
      172.16.127.254 (Last IP)
       172.16.127.255 (Broadcast IP)
------------------------------------------------------------------------------------
172.16.128.0 (Second network)
172.16.128.1 (First IP)
*
 172.16.255.254 (Last IP)
 172.16.255.255 (Broadcast IP)
Subnet mask ==> 255.255.128.255

---
IP v6 :-
128 bit address.
e.g. 2001:0db8:0a0b:12f0:0000:0000:0000:0001
Each group of 16 bit.
Doesn’t have concept of broadcast.
Doesn’t have concept of NAT.
Doesn’t have concept of Subnetting.
Special IP’s :-
Loop back address :- “:: 01” or “::1”
Invalid IP :- 0000:0000:0000:0000:0000:0000:0000:0000 or ::
Multicast IP :- FF80::
Link Local IP : FE80::
Global Unicast :- 2000::
Unique Local :- FC00::

---
THANK YOU … !!!